## Slide 1: طراحی سيستم های ديجيتال برنامه پذير

## Slide 2: طراحی سيستم های ديجيتال برنامه پذير
Text Book:
م. صاحب‌الزمانی، طراحی کامپیوتری سیستم‌های دیجیتال، نشر شیخ بهایی، 1398
References:
P. Simpson, FPGA Design: Best Practices for Team-Based Reuse, Springer, 2nd Edition, 2015.
U. Heinkel et. al, The VHDL Reference: A Practical Guide to Computer-Aided Integrated Circuit Design including VHDL-AMS, Wiley, 2000.
Clive Maxfield, The Design Warrior’s Guide to FPGA, Elsevier, 2004.
E. Stavinov, 100 Power Tips for FPGA Designers, 2011.
Z. Salcic, A. Smailagic, Digital Systems Design and Prototyping Using Field-Programmable Logic and Hardware Description Languages, 2nd Edition, 2000.
Datasheets + References given in the slides

## Slide 3: تراشه‌هاي منطقي برنامه‌پذير
Marking
  Homework sets
  Quizzes
  Project
  Midterm Exam
  Final Exam
Software
  Vivado
  ModelSim

## Slide 4: Digital Systems
Digital systems implementation:
  Conventionally on CPU
  Need for high speed
     Increase frequency
     Multi-core
     Many-core (GPU)
  Not enough speed for some applications
  High power consumption

## Slide 5: Technology Trend
Till 2005, transistor counts increased by Moore law

## Slide 6: Technology Trend

## Slide 7: Technology Trend
Till 2005, transistor counts increased by Moore law
Increasing number of cores instead of transistors
Predicted that multicore scaling may stop

## Slide 8: Hardware vs. Software
Software
  Slow:
    Sequential: one instruction/operation at a time
    Must fetch and execute each instruction
    Memory bottleneck
      Caches only mitigate the bottleneck
  Easy to write, easy to debug, easy to modify

## Slide 9: Hardware vs. Software
Hardware
  Fast; no instruction fetch, decode, …
  Can easily expose parallelism
  More difficult to design, debug and modify

## Slide 10: The Von Neumann Computer
Sequential execution
  tcycle = cycle execution time
One instruction needs tinstruction = 5*tcycle
3 instructions: in 15*tcycle
Pipelining:
One instruction needs tinstruction = 5*tcycle
  no improvement
3 instructions: in 7*tcycle in the
ideal case.
 Increased throughput
Even with pipeline, cache, etc., execution remains sequential.
  if (a < b) then
  {
    d = a+b;
    c = a*b;
  }
  else
  {
    d = a+1;
    c = b-1;
  }

## Slide 11: Hardware Implementation
Hardware Example:
Implementation of a VN computer:
  if (a < b) then
  {
    d = a+b;
    c = a*b;
  }
  else
  {
    d = a+1;
    c = b-1;
  }
At least 3 instructions
run-time >= 3*tinstruction
Complete execution in
parallel in one clock cycle
run-time = tclock= delay of longest path from input to output

## Slide 12: HW vs. SW Implementation Example

## Slide 13: مدارهاي ديجيتال

## Slide 14: Programmable Logic Array (PLA)

## Slide 15: PLA

## Slide 16: PLA

## Slide 17: PAL
W = AB’ C’ + CD
X = A’BC’ + A’CD + ACD’ + BCD
Y = A’C’D + ACD + A’BD
فقط AND Plane قابل برنامه ريزي.

## Slide 18: Programmable Array Logic (PAL)
PAL 16R8
براي پياده‌سازي مدارهاي ترتيبي معمولا در خروجي، FF قرار دارد.

## Slide 19: PAL 16R8

## Slide 20: PAL 16R8

## Slide 21: Simple PLD (SPLD) (22V10)

## Slide 22: SPLD Macrocell

## Slide 23: CPLD
Interconection Wires

## Slide 24: بخشي از CPLD

## Slide 25: ساختار FPGA

## Slide 26: ساختار FPGA

## Slide 27: Logic Cell

## Slide 28: LUT

## Slide 29: مثال
با LUTهای سه ورودی
F(a, b, c, d, e) = (a + b) . (c + d' . e')
F1 = a + b
F2 = c + d' . e'
F = F1 . F2

## Slide 30: مثال
با LUTهای سه ورودی
F(a, b, c, d, e) = (a + b) . (c + d' . e')
F1 = a + b
F2 = c + d' . e'
F = F1 . F2

## Slide 31: مثال
با LUTهای سه ورودی
F(a, b, c, d, e) = (a + b) . (c + d' . e')
F1 = c + d' . e'
F2 = (a + b).F1

## Slide 32: Logic Cell نمونه
Spartan Logic Cell

## Slide 33: ساختار FPGA

## Slide 34: Programmable Switch Matrix (PSM)

## Slide 35: SRAM-Based FPGA
[Entegra]
Programmable Logic Blocks
Programmable routing structure