## Slide 1: زبان توصیف سخت‌افزار
Hardware Description Language

## Slide 2: زبان‌ها
  VHDL
    یادگیری حداقل یک زبان به طور کامل
      یادگیری ناقص و سعی و خطا  سخت شدن توصیف و اشکال‌زدایی
    VHDL/Verilog: اصول یکسان – ساختارهای نحوی متفاوت
    VHSIC HDL (اوایل دهة 1980)
    مبتنی بر زبان ADA

## Slide 3: VHDL
کاربردها:
  مستندسازی (documentation)
  مدل‌سازی (modeling)
  سنتز و پیاده‌سازی (synthesis and implementation)
  درستی‌سنجی (verification)

## Slide 4: VHDL
کاربردها:
  مستندسازی (طرز کار سخت‌افزار یا تراشه مشخص):
    به جای توصیف زبان طبیعی:
      نادقیق (برداشت‌های مختلف)
      غیر قابل پردازش

## Slide 5: VHDL
کاربردها:
  مدل‌سازی:
    مراحل اولیة طراحی:
      عملکرد و رفتار کلی مشخص است
      توصیف الگوریتم با دستورهای رفتاری
      کمک به فهم صورت مسأله
      جلوگیری از سرایت اشکالات به سطوح پایین طراحی

## Slide 6: VHDL
کاربردها:
  مدل‌سازی:
    مثال: کنترل‌کنندة آسانسور
...
while (true) loop
begin
...
if (REQUEST = true)then
if (REQUEST_FLOOR > CURRENT_FLOOR) then
MOVE_UP (CURRENT_FLOOR, ...);
else
MOVE_DOWN (CURRENT_FLOOR, ...);
end if;
end if;
...
end loop;
...

## Slide 7: VHDL
کاربردها:
  سنتز و پیاده‌سازی
    تولید خودکار مدار از توصیف
    زیرمجموعة قابل سنتز
      لزوم آشنایی با این زیرمجموعه
      تفاوت ابزارها  portable code
        کد غیر قابل سنتز برای دیگری
        مدار متفاوت
      کلیات یکسان
    این درس:
      موارد کلی مشترک
      نحوة کدنویسی مناسب

## Slide 8: VHDL
کاربردها:
  درستی‌سنجی
    محیط درستی‌سنجی: testbench
    عناصر اصلی:
      طرح مورد آزمون
      تولید و اِعمال بردارهای ورودی
      مشاهده و تحلیل خروجی‌ها

## Slide 9: VHDL
کاربردها:
  درستی‌سنجی
    تولید بردارهای ورودی (بردارهای آزمون یا test vectors):
      همه ورودی‌های ممکن
      تصادفی
      انتخاب هوشمندانه با پیاده‌سازی الگوریتم
    نیاز به توصیف با کد VHDL
      برنامه‌نویسی روالی
      خواندن از فایل

## Slide 10: VHDL
  مثال:
    سخت‌افزار محاسبة (x2 + y2)
    مقایسه با نتیجة رفتاری
architecture TBENCH of ENT_BENCH is
procedure WAVE_GEN (signal X:out integer, signal Y:out integer)
variable I integer:= 0;
begin
for VX in 0 to 63 loop
for VY in 0 to 63 loop
begin
X <= VX after I*10 ns;
Y <= VY after I*10 ns;
I:= I + 1;
end loop;
end procedure WAVE_GEN;
begin
WAVE_GEN (X, Y);
L1:L_MODULE port map(X,Y,L);
L_BEHAVE <= (X**2 + Y**2);
ERROR_SIG <= L_BEHAVE xor L;
end architecture TBENCH;

## Slide 11
نصب نرم‌افزار ویوادو
  h.malakouty@gmail.com
  نصب تا سه شنبه آینده

## Slide 12: سطوح تجرید (Levels of Abstraction)

## Slide 13: سطوح تجرید (Levels of Abstraction)

## Slide 14: سطوح تجرید (Levels of Abstraction)

## Slide 15: سطوح تجرید (Levels of Abstraction)

## Slide 16: سطوح تجرید (Levels of Abstraction)

## Slide 17: سطوح تجرید (Levels of Abstraction)
رفتاری:
    توصیف عملکرد مطلوب (الگوریتمی)
    بدون پرداختن به مدار
    همة امکانات VHDL
    قابل نمایش با روندنما (flow chart)

## Slide 18: سطوح تجرید: سطح رفتاری
رفتاری:
    تولید سیگنال ساعت c2 از ساعت c1 برای ساعت‌زنی ناهمپوشان دوفازی

## Slide 19: سطوح تجرید: سطح رفتاری
رفتاری:
  کد FM0 برای RFID (Differential Manchester Encoding)
    ارسال و دریافت با خطای کمتر و بازیابی کلاک:
    din = 1  تغییر حالت خروجی +ms 10 ثابت
    din = 0  تغییر حالت خروجی +ms 5 ثابت + تغییر حالت خروجی + ms 5 ثابت

## Slide 20: سطوح تجرید: سطح رفتاری
while (END_OF_DATA(...)) loop
READ_DATA(DIN);
if (DIN = '1') then
DOUT <= not DOUT;
wait for 10 ms;
else
DOUT <= not DOUT;
wait for 5 ns;
DOUT <= not DOUT;
wait for 5 ns;
end if;
end loop;

## Slide 21: سطوح تجرید: سطح انتقال ثبات
سطح انتقال ثبات (Register-Transfer Level) RTL:
  مسیر داده
    ثبات‌ها
    مدارهای ترکیبی (محاسباتی و منطقی)
    منابع ارتباط دهنده‌ بین آنها
      گذرگاه
      مالتی‌پلکسر
      سیم
      ...
  کنترل‌کننده (مسیر کنترل)
    ماشین حالت متناهی FSM

## Slide 22: سطوح تجرید: سطح انتقال ثبات
انتقال ثبات:
process (CLK)
begin
if (CLK’event and CLK = ’1’) then
Z <= D;
end if;
end process;
process (A, B, M)
begin
if (M = '1‘) then
D <= A * B;
else
D <= A – B;
end if;
end process;

## Slide 23: سطوح تجرید: سطح انتقال ثبات
انتقال ثبات:
  کد FM0

## Slide 24: سطوح تجرید: سطح انتقال ثبات
انتقال ثبات:
  کد FM0

## Slide 25: سطوح تجرید: سطح انتقال ثبات
انتقال ثبات:
  کد FM0
CONTROL_P:process(CLK)
begin
if rising_edge(CLK) then
if RST = '1' then
STATE <= S11;
else
case STATE is
when S11 =>
if DIN = '0' then
STATE <= S01;
else
STATE <= S00;
end if;
when S01 =>
…
end case;
end if;
end if;
end process CONTROL_P;
DATA_P:process(STATE, CLK)
begin
if CLK = '0' then
DOUT <= STATE(0);
else
DOUT <= STATE(1);
end if;
end process DATA_P;

## Slide 26: سطح انتقال ثبات: مثال
محاسبه ب.م.م در سطح انتقال ثبات:
مسیر داده
int gcd(int x, int y)
{
fin = false;
while (!fin)
{
if (x > y)
x = x – y;
else if (x < y)
y = y – x;
else
fin = true;
}
return x;
}

## Slide 27: سطح انتقال ثبات: مثال
int gcd(int x, int y)
{
fin = false;
while (!fin)
{
if (x > y)
x = x – y;
else if (x < y)
y = y – x;
else
fin = true;
}
return x;
}

## Slide 28: سطوح تجرید: سطح گیت
گیت:
architecture GATE_LEVEL of ADDER is …. begin L1:XORG port map(X1, Y1, T1); L2:ANDG port map(X1, Y1, T2); L3:XORG port map(T1, Z, S1); L4:ANDG port map(T1, Z, T3);
L5:ORG port map(T3, T2, C1);
….
end GATE_LEVEL;

## Slide 29: توصیف سخت‌افزار با VHDL
جزئیات:
  Language Reference Manual
    به عنوان مرجع اصلی
    1076 LRM Ieee Standard Vhdl Language Reference Manual.pdf
  VHDL-AMS 1076.1
    فقط شبیه‌سازی
    نحوة شبیه‌سازی: معادلات دیفرانسیل

## Slide 30: VHDL Structural Elements
Entity: نحوه ارتباط با ساير پودمان‌ها
Architecture: عملکرد یا بدنه
Configuration: ایجاد ارتباط با عناصر کتابخانه
Process: اجرای ترتیبی
Package: مجموعه اجزای سخت‌افزاری، مجموعه ثابت‌ها و انواع داده یا زیربرنامه‌ها
Library: گروهی از واحدهای کامپایل شده

## Slide 31: Entity
entity HALF_ADDER is
port (A, B: in bit; S, Cout: out bit);
end entity HALF_ADDER;
Interface description
No behavior/implementation definition
entity ADDER is port( A, B: in bit_vector (3 downto 0); SUM: out bit_vector (3 downto 0);
CARRY: out bit ); end ADDER;
Linking via port signals
  data types
  signal width
  signal direction
in integer range 15 downto 0; out integer range 15 downto 0;

## Slide 32: Architecture
entity HALF_ADDER is
port (A, B: in bit; S, Cout: out bit);
end entity HALF_ADDER;
architecture RTL of HALF_ADDER is
begin
SUM <= A xor B;
CARRY <= A and B;
end architecture RTL;
Implementation of the design
Always connected with a specific entity
  one entity can have several architectures
  entity ports are available as signals within the architecture
Contains concurrent statements

## Slide 33: Architecture Structure
architecture RTL of STRUCTURE is constant BASE: integer := 10; subtype DIGIT is integer range 0 to 9; signal DIGIT_A, DIGIT_B: DIGIT; signal CARRY: DIGIT;
begin DIGIT_A <= 3; SUM <= DIGIT_A + DIGIT_B; DIGIT_B <= 7; CARRY <= 0 when SUM < BASE else 1; end EXAMPLE ;
Declarative part:
  data types
  constants
  intermediate signals
  ...
Statement part (after 'begin'):
  signal assignments
  processes
  component instantiations
  concurrent statements: order not important
   Simulator recalculates sum any time an operand changes
Port is a kind of signal.

## Slide 34: Entity Port Modes
in:
  signal values are read-only
out:
  signal values are write-only
  multiple drivers
buffer:
  similar to out
  signal values may be read from inside
  only 1 driver
inout:
  bidirectional port
Output port modes have to match.

## Slide 35: Use of VHDL Objects

## Slide 36: Structural Model

## Slide 37: Component Declaration
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component;
component ORGATE port (X, Y : in bit; RES : out bit); end component;
signal W_SUM, W_CARRY1, W_CARRY2 : bit;
begin
. . .
In declarative part of architecture
entity HALFADDER is port( X, Y: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( X, Y: in bit; RES: out bit); end entity ORGATE;

## Slide 38: Component Instantiation
architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component; component ORGATE port (X, Y : in bit; RES : out bit); end component; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1: HALFADDER port map( A, B, W_SUM, W_CARRY1 ); MODULE2: HALFADDER port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 ); MODULE3: ORGATE port map ( W_CARRY2, W_CARRY1, CARRY );
end STRUCT;
May need many of each
Instantiation in statement part of architecture (after 'begin')
Wires signals together:
  default: positional association
X
Y
X
Y
SUM
CARRY
SUM
CARRY
X
Y
RES

## Slide 39: Named Signal Association
entity FULLADDER is port (A,B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HALFADDER port (X, Y : in bit; SUM, CARRY : out bit); end component; . . . signal W_SUM, W_CARRY1, W_CARRY2 : bit; begin MODULE1: HALFADDER port map ( X => A, SUM => W_SUM, Y => B, CARRY => W_CARRY1 ); . . . end STRUCT;
Named association:
  left side: "formals" (port names from component declaration)
  right side: "actuals" (architecture signals)
Independent of order in component declaration
X
Y
X
Y
SUM
CARRY
SUM
CARRY
X
Y
RES

## Slide 40: توصیف ساختاری
ساختاری (structural):
⋮
begin
FA1:FULL_ADDER port map (C0, A0, B0, S0, C1);
FA2:FULL_ADDER port map (C1, A1, B1, S1, C2);
FA3:FULL_ADDER port map (C2, A2, B2, S2, C3);
FA4:FULL_ADDER port map (C3, A3, B3, S3, C4);
end;
⋮

## Slide 41: Configuration
architecture … component HA port(X, Y: in bit; SUM, CARRY: out bit); end HA; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin
· · · MODULE1 : HA port map(A, B, W_SUM, W_CARRY1);
MODULE2: HA port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 );
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( A, B: in bit; RES: out bit); end entity ORGATE;
architecture RTL of HALFADDER is begin
…
end architecture RTL;
architecture RTL of ORGATE is begin
…
end architecture RTL;
Library (work)

## Slide 42: Configuration
architecture … component HA port(X, Y: in bit; SUM, CARRY: out bit); end HA; signal W_SUM, W_CARRY1, W_CARRY2: bit; begin
· · · MODULE1: HA port map(A, B, W_SUM, W_CARRY1);
MODULE2: HA port map ( W_SUM, CARRY_IN, SUM, W_CARRY2 );
Entities may be instantiated directly without preceding component declaration
(Not recommended)
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
entity ORGATE is port( A, B: in bit; RES: out bit); end entity ORGATE;
architecture RTL of HALFADDER is begin
…
end architecture RTL;
architecture RTL of ORGATE is begin
…
end architecture RTL;
Library (work)
for MODULE1: HA use entity work.HALFADDER (RTL);
for MODULE2: HA use entity work.HALFADDER (RTL);
In Vivado: xil_defaultlib

## Slide 43: Configuration
Selects entity/architecture pairs for instantiated components
Generates the hierarchy
Default binding rules:
  selects entity with the same name as component
  last compiled architecture is used

## Slide 44: Simple Configuration Specification
entity FULLADDER is port(A, B, CARRY_IN: in bit; SUM, CARRY: out bit); end FULLADDER; architecture STRUCT of FULLADDER is component HA port(A, B: in bit; SUM, CARRY: out bit); end component;
for MODULE1:HA
use entity work.HALFADDER (RTL);
for MODULE2:HA
use entity work.HALFADDER (GATE);
signal W_SUM, W_CARRY1, W_CARRY2: bit; begin MODULE1:HA port map (…, …); MODULE2:HA port map(…, …);
end STRUCT;
entity HALFADDER is
port(A,B: in bit; S, CY: out bit); end A;
architecture RTL of HALFADDER is · · ·
end RTL;
architecture GATE of HALFADDER is · · ·
end GATE;
Library (work)
  instance names
  'all': all instances of the specified component
  'others': all instances not explicitly mentioned

## Slide 45: Configuration Declaration
configuration CFG_FULLADDER of FULLADDER is for STRUCT for MODULE2:HA use entity work.HALFADDER(GATE); end for; for others:HA use entity work.HALFADDER(RTL); end for; end for; end CFG_FULLADDER;
Possible to reference an existing configuration of a submodule
configuration CONFNAME of ENTITYNAME is
for ARCHNAME
for INSTANCENAME use entity LIBNAME.ENTNAME(ARNAME);
for all:FA use configuration work.CFG_FULLADDER;

## Slide 46: Configuration

## Slide 47: Configuration Specification
architecture STRUCTL of SIXTEEN_BIT_ADDER is
component ADDER4BIT
port (A,B: …;
…);
end component;
signal …;
for A1,A2:ADDER4BIT
use entity work.FOUR_BIT_ADDER(CARRY_RIPPLE_ADDER);
for others:ADDER4BIT
use entity work.FOUR_BIT_ADDER(CARRY_LOOKAHEAD_ADDER);
begin
A1:ADDER4BIT port map (…);
A2:ADDER4BIT port map (…);
A3:ADDER4BIT port map (…);
A4:ADDER4BIT port map (…);

## Slide 48: Configuration Declaration
configuration CONFING_EXAMPLE of SIXTEEN_BIT_ADDER is
for STRUCTL
for A1,A2:ADDER4BIT use
entity work.FOUR_BIT_ADDER(CARRY_RIPPLE_ADDER);
for CARRY_RIPPLE_ADDER
for all:FADD use
entity work.FULL_ADDER(FARCH1);
end for;
end for;
end for;
for others:ADDER_4BIT use
entity work.FOUR_BIT_ADDER(CARRY_LOOKAHEAD_ADDER);
end for;
end for;
end configuration CONFING_EXAMPLE;
configuration CONFNAME of ENTITYNAME is
for ARCHNAME
for INSTANCENAME use entity LIBNAME.ENTNAME(ARNAME);

## Slide 49: جمع‌بندی
  توصيف ساختاري functionality را صريحاً توصيف نمي‌كند بلكه فقط ليستي از اجزا و نحوة اتصال آنهاست.
  معمولاً برای توصیف بالاترین سطح از این توصیف استفاده می‌شود.
    مثال: لایه‌های شبکه عصبی

## Slide 50: جمع‌بندی