## Slide 1: زبان توصیف سخت‌افزار
Hardware Description Language

## Slide 2: عملکرد همروند و عملکرد ترتیبی
  عملکرد ترتیبی:
    اجرا به ترتیب از بالا به پایین
    مانند اکثر زبان‌های نرم‌افزاری
    برای عملکرد ترتیبی، در بدنه‌های ترتیبی
      process
      procedure
      function
  عملکرد همروند:
    عملکرد واقعی سخت‌افزار
    عملکرد پیش‌فرض در architecture

## Slide 3: عملکرد همروند و عملکرد ترتیبی
  دستورهای همروند:
    فقط در بدنة همروند
      ایجاد یک پودمان (module instantiation)
      انتساب به سیگنال
      فرایند (process)
      if/for generate
      when-else
      with-select-when
      فراخوانی روال
      فراخوانی تابع

## Slide 4: عملکرد همروند و عملکرد ترتیبی
  دستورهای ترتیبی:
    فقط در بدنة ترتیبی
      if-then-else
      حلقة for
      حلقة while
      case-when
      انتساب به سیگنال
      فراخوانی روال
      فراخوانی تابع

## Slide 5: ساختارهای منظم
for-generate:
  برای توصیف طرح‌های منظم
entity FOUR_BIT_ADDER is
port (A , B : in bit_vector (3 downto 0);
CIN : in bit;
S : out bit_vector (3 downto 0);
COUT : out bit);
end entity FOUR_BIT_ADDER;
--
architecture STRUCT_FA of FOUR_BIT_ADDER is
component FULL_ADDER port (X , Y , CI : in bit ; Z , CO : out bit);
end component;
signal C : bit_vector (3 downto 1);
begin
FA0: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA1: FULL_ADDER port map (A(1), B(1), C(1), S(1), C(2));
FA2: FULL_ADDER port map (A(2), B(2), C(2), S(2), C(3));
FA3: FULL_ADDER port map (A(3), B(3), C(3), S(3), COUT);
end architecture STRUCT_FA;
CIN
CO

## Slide 6: ساختارهای منظم
entity FOUR_BIT_ADDER is
...
end entity FOUR_BIT_ADDER;
--
architecture STRUCT_FA of FOUR_BIT_ADDER is
...
begin
FA0: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA3: FULL_ADDER port map (A(3), B(3), C(3), S(3), COUT);
F: for I in 2 downto 1 generate FAS: FULL_ADDER port map(A(I), B(I), C(I), S(I), C(I+1));
end generate F;
end architecture STRUCT_FA;
FA0: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA1: FULL_ADDER port map (A(1), B(1), C(1), S(1), C(2));
FA2: FULL_ADDER port map (A(2), B(2), C(2), S(2), C(3));
FA3: FULL_ADDER port map (A(3), B(3), C(3), S(3), COUT);

## Slide 7: ساختارهای منظم
entity FOUR_BIT_ADDER is
...
end entity FOUR_BIT_ADDER;
--
architecture STRUCT_FOR of FOUR_BIT_ADDER is
signal C : bit_vector (3 downto 1);
begin
F: for I in 3 downto 0 generate F_IF0: if I=0 generate L0:FULL_ADDER port map(A(0), B(0), CIN, S(0), C(1));
end generate F_IF0;
F_IF3 : if I=3 generate L3:FULL_ADDER port map(A(3), B(3), C(3), S(3), COUT);
end generate F_IF3;
F_IF_1_2 : if I/=3 and I/=0 generate L_1_2:FULL_ADDER port map(A(I), B(I), C(I), S(I), C(I+1));
end generate F_IF_1_2;
end generate F;
end architecture STRUCT_FOR;
FA0: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA1: FULL_ADDER port map (A(1), B(1), C(1), S(1), C(2));
FA2: FULL_ADDER port map (A(2), B(2), C(2), S(2), C(3));
FA3: FULL_ADDER port map (A(3), B(3), C(3), S(3), COUT);
if-generate:

## Slide 8: ساختارهای منظم
entity FOUR_BIT_ADDER is
...
end entity FOUR_BIT_ADDER;
--
architecture STRUCT_FOR of FOUR_BIT_ADDER is
signal C : bit_vector (4 downto 0);
begin
F: for I in 3 downto 0 generate FAS: FULL_ADDER port map(A(I), B(I), C(I), S(I), C(I+1));
end generate F;
COUT <= C(4);
C(0) <= CIN;
end architecture STRUCT_FOR;
FA0: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA1: FULL_ADDER port map (A(1), B(1), C(1), S(1), C(2));
FA2: FULL_ADDER port map (A(2), B(2), C(2), S(2), C(3));
FA3: FULL_ADDER port map (A(3), B(3), C(3), S(3), COUT);
CIN
CO

## Slide 9: طراحی به صورت کلی
طراحی کلی:
  محدود نبودن به حالت خاص
    شمارنده صفر تا n-1
    جمع‌کنندة n-بیتی
    مقایسه‌کنندة n-بیتی

## Slide 10: طراحی به صورت کلی
جمع‌کنندة n-بیتی:
  با ثابت‌ها:
entity N_BIT_ADDER IS
port( A , B : in bit_vector (N-1 downto 0);
CIN : in bit;
S : out bit_vector(N-1 downto 0);
COUT : out bit);
end entity N_BIT_ADDER;
architecture STRUCT_FOR of N_BIT_ADDER is
component FULL_ADDER port (X , Y , CI : in bit ; Z , CO : out bit);
end component;
signal C : bit_vector (N-1 downto 0);
begin
FA1: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA_N: FULL_ADDER port map (A(N-1) ,B(N-1) ,C(N-1) ,S(N-1) ,COUT );
L: for I in N-2 downto 1 generate FAS: FULL_ADDER port map(A(I) ,B(I) ,C(I) ,S(I) ,C(I+1));
end generate L;
end architecture STRUCT_FOR;
constant N : integer :=4;

## Slide 11: طراحی به صورت کلی
جمع‌کنندة n-بیتی:
  با ثابت‌ها
    اشکال:
      برای هر مورد، نیاز به کامپایل مجدد
      برای چند مورد، نیاز به کپی کد

## Slide 12: طراحی به صورت کلی
  با پارامتر generic
entity N_BIT_ADDER IS
generic (N : integer := 4);
port(A ,B : in bit_vector (N-1 downto 0);
CIN : in bit;
S : out bit_vector(N-1 downto 0);
COUT : out bit);
end entity N_BIT_ADDER;
architecture STRUCT_FOR of N_BIT_ADDER is
component FULL_ADDER port (X , Y , CI : in bit ; Z , CO : out bit);
end component;
signal C : bit_vector (N-1 downto 0);
begin
FA1: FULL_ADDER port map (A(0), B(0), CIN, S(0), C(1));
FA_N: FULL_ADDER port map (A(N-1) ,B(N-1) ,C(N-1) ,S(N-1) ,COUT );
L: for I in N-2 downto 1 generate FAS: FULL_ADDER port map(A(I) ,B(I) ,C(I) ,S(I) ,C(I+1));
end generate L;
end architecture STRUCT_FOR;
...
begin
INST1:N_BIT_ADDER generic map (8) port map (...);
INST2:N_BIT_ADDER generic map (64) port map (...);
end architecture STRUCT_FOR;

## Slide 13: طراحی به صورت کلی
  بدون مشخص کردن بازه درگاه‌ها (با attribute)
    برای سیگنال‌ها نمی‌توان نامشخص گذاشت.
entity GENERAL_ADDER IS
port(A ,B : in bit_vector (N-1 downto 0);
CIN : in bit;
S : out bit_vector (N-1 downto 0);
COUT : out bit);
end entity GENERAL_ADDER;
architecture ARCH1 of GENERAL_ADDER is
component FULL_ADDER port (X , Y , CI : in bit ; Z , CO : out bit);
end component;
signal C : bit_vector (???);
begin
FA1: FULL_ADDER port map (A(???), B(???), CIN, S(???), C(???));
FA_N: FULL_ADDER port map (A(???), B(???), C(???), S(???), COUT );
L: for I in ??? downto ??? generate FAS: FULL_ADDER port map(A(I), B(I), C(I), S(I), C(I+1));
end generate L;
end architecture ARCH1;
      چگونه اندیس حلقة for-generate را بدهیم؟
      چگونه در instantiation مشخص کنیم کدام است؟

## Slide 14: طراحی به صورت کلی
  بدون مشخص کردن بازه درگاه‌ها (با attribute)
    برای سیگنال‌ها نمی‌توان نامشخص گذاشت.
entity GENERAL_ADDER IS
port(A ,B : in bit_vector (N-1 downto 0);
CIN : in bit;
S : out bit_vector (N-1 downto 0);
COUT : out bit);
end entity GENERAL_ADDER;
architecture ARCH1 of GENERAL_ADDER is
component FULL_ADDER port (X , Y , CI : in bit ; Z , CO : out bit);
end component;
signal C : bit_vector (A’range);
begin
FA1: FULL_ADDER port map (A(A’low), B(A’low), CIN, S(A’low), C(A’low+1));
FA_N: FULL_ADDER port map (A(A’high), B(A’high), C(A’high), S(A’high), COUT );
L: for I in A’high-1 downto A’low+1 generate FAS: FULL_ADDER port map(A(I), B(I), C(I), S(I), C(I+1));
end generate L;
end architecture ARCH1;
      چگونه اندیس حلقة for-generate را بدهیم؟
      چگونه در instantiation مشخص کنیم کدام است؟

## Slide 15: طراحی به صورت کلی
  بدون مشخص کردن بازه درگاه‌ها (با attribute)
architecture ...
signal S1, S2, S3: bit_vector (7 downto 0);
signal S4, S5, S6: bit_vector (3 downto 0);
signal CIN1, CIN2, COUT1, COUT2: bit;
begin
...
EIGHTBIT:GENERAL_ADDER port map (S1, S2, CIN1, S3, COUT1);
FOURBIT:GENERAL_ADDER port map (S4, S5, CIN2, S6, COUT2);
end architecture STRUCT_FOR;
  اگر درگاه‌ها به درگاه‌های سطح بالاتر وصل بود چطور؟